SIF Transportation and Geographic Information Working Group

Object Plan

Version 1.1

July 25, 2007

SIF Change Proposal and Plan:

StudentTransportInfo

Submitted by:	Transportation and Geographic Information Working Group

Version:	v1.0

Date Submitted:

Table of Contents

Change Proposal	3

Rationale for Change	3

Business Case	3

Time Line	3

Change Plan	3

Object Dependencies and Relation Map	3

Changes to Other Objects	4

Infrastructure Changes	4

Object Definition	5

Issues	8

XML Example	9

Use Cases	9

StudentTransportInfo - Request	9

StudentTransportInfo – Change event processing	10

| Draft Specification Document Version Control |
| --- |
| Version | Date: | Author/Organization: | Comments |
| v0.1 | 6/19/2007 | K.Ziarko/VersaTrans Solutions, Inc. | Initial draft of object proposal section. |
| V0.2 | 6/26/2007 | K.Ziarko/VersaTrans Solutions, Inc. | Prepared document for submission. |
| V0.2 | 6/26/2007 | Laurie Collins | Review for submission |
| V1.0 | 7/25/2007 | K.Ziarko/VersaTrans Solutions, Inc. | Added object plan details. |
| V1.1 | 10/1/2007 | K.Ziarko/VersaTrans Solutions, Inc. | Made mandatory fields optional; removed Transfer point sequence number. |

# Change Proposal

# Rationale for Change

Currently, agents need to subscribe to multiple transportation objects to obtain basic details regarding a student’s transportation.  The changes outlined in the proposal will eliminate the need to process other objects if they are not needed by the subscribing agent/application.  The goal of these changes is to make the student’s transportation detail information more easily accessible to subscribers.

In addition, there are new elements and clarifications needed by subscribing agents which will be added to the StudentTransportInfo object.  There are also elements which cause confusion to subscribers based on their naming and description.  The HomeBusRouteDetail  and SchoolBusRouteDetail will be deprecated, and replaced by the OriginPoint and DestinationPoint elements.

# Business Case

The goal of the proposed changes is to provide information in a more accessible manner to subscribing agents.  With these changes, a subscriber that is interested in specific details of a student’s daily transportation information will no longer have to subscribe to the BusInfo, BusStopInfo, BusRouteInfo, and BusRouteDetail objects.  The details that a Student Information System, or other subscriber would be interested in regarding a student’s daily transportation will be accessible through the StudentTransportInfo object.  In addition, the new elements that are proposed will provide additional details that will further define the object as requested by existing implementations.

# Time Line

This modification will be implemented as part of the SIF Implementation Specification 2.2.

# Change Plan

# Object Dependencies and Relation Map

# Changes to Other Objects

There are no changes needed to other objects to support this change.

# Infrastructure Changes

There are no changes needed to infrastructure to support this change.

## Object Definition

Insert Object text definition here:

|  | Element/@Attribute | Char | Description | Type |
| --- | --- | --- | --- | --- |
|  | StudentTransportInfo |  | This object contains transportation information about a student. Students should have at least two StudentTransportInfo objects associated with them: one for inbound information (getting to school) and one for outbound information (leaving school). If their transportation changes based on the day of the week, then a student will have more than two StudentTransportInfo objects. |  |
| @ | RefId | M | GUID that identifies this object. | RefIdType |
| @ | StudentPersonalRefId | M | GUID that identifies the student that this object refers to | IdRefType |
| @ | Type | M | The direction of transportation that this object refers to. | Values: Inbound Outbound |
| @ | DayOfWeek | M | This attribute indicates the day(s) of the week to which this object refers | xs:token xs:pattern :(Mo)?(Tu)?(We)?(Th)?(Fr)?(Sa)?(Su)? |
| @ | SchoolInfoRefId | M | GUID referring to the school that the student attends on these day(s) of the week. | IdRefType |
|  | StateAidQualification | O | The qualification status of a student entitling local education agency to receive state transportation aid. Values Source: 0720 (State Transportation Aid Qualification) | NCES0720StateTransportationAidQualification |
|  | TransportationStatus | O | Information about whether or not a student is transported to and/or from school or receives services, aid, or payment in lieu of transportation. Values Source: 0719 (Transportation Status) | NCES0719TransportationStatus |
|  | PublicExpense | O | The eligibility of a student for transportation between home and school at local public expense because of distance, disability, or other reasons. Values Source: 0721 (Transportation at Public Expense Eligibility) | NCES0721TransporationatPublicExpenseEligibility |
|  | HomeToSchoolDistance | O | Distance between the student’s home address and the school. | xs:decimal |
| @ | Unit | M | Units used in distance reporting. | values: km Kilometers m Miles |
|  | WalkToStopDistance | O | Distance between the student’s address and the bus stop where they are picked up or dropped off. | xs:decimal |
| @ | Unit | M | Units used in distance reporting. | values: km Kilometers m Miles |
|  | StopToSchoolDistance | O | Distance between the bus stop where a student is picked up or dropped off and the school | xs:decimal |
| @ | Unit | M | Units used in distance reporting. | values: km Kilometers m Miles |
|  | Eligibility | O | Eligibility status of student for district transportation for this trip. Note: this element has been deprecated – use TransportationStatus and PublicExpense. | Values: Bus Walk BusHazard BusOutOfAttendance ParentPay Unknown |
|  | OriginPoint | O | GUID that identifies the bus stop/route where the student gets on the bus. | IdRefType |
| @ | SIF_RefObject | M |  | values: BusRouteDetail |
|  | OriginPoint/ArrivalTime | O | The time that the bus associated with this route will stop at this bus stop. | xs:time |
|  | OriginPoint/RouteNumber | O | A unique identifier for the route. For instance, you may have route 16AM in the morning and a 16PM in the afternoon. | xs:normalizedString |
|  | OriginPoint/RouteDescription | O | Short explanation of the route. | xs:string |
|  | OriginPoint/VehicleNumber | O | Vehicle number of the bus. | xs:normalizedString |
|  | OriginPoint/BusStopDescription | O | An explanation of this location. | xs:string |
|  | HomeBusRouteDetail | O | Note: this element will be deprecated in a future version – Use Origin and Destination Points. GUID referring to a BusRouteDetail object that identifies the origin bus stop for an inbound route or the destination bus stop for an outbound route. If the HomeBusRouteDetail element does not exist, then the student does not ride a bus to/from school. | IdRefType |
| @ | SIF_RefObject | M | . | Values: BusRouteDetail |
|  | TransferPoints | O |  | List |
|  | TransferPoints/TransferPoint | OR | There should be one TransferPoint element for each intermediate point on a trip. The “embark” and “disembark” bus stops for a single transfer point must be at the same location. To order multiple TransferPoint elements, use the Time element of the BusStopInfo objects referenced by the attributes |  |
|  | TransferPoints/TransferPoint/EmbarkBusRouteDetail | M | GUID that identifies the bus stop/route where the student gets on the bus. | IdRefType |
| @ | SIF_RefObject | O | . | Values: BusRouteDetail |
|  | TransferPoints/TransferPoint/DisembarkBusRouteDetail | M | GUID that identifies the bus stop/route where the student gets off the bus | IdRefType |
| @ | SIF_RefObject | M |  | Values: BusRouteDetail |
|  | SchoolBusRouteDetail | O | Note: this element will be deprecated in a future version – Use Origin and Destination Points. GUID referring to a BusRouteDetail object that identifies the origin bus stop for an outbound route or the destination bus stop for an inbound route. If the SchoolBusRouteDetail does not exist, then the student does not ride a bus to/from school. | IdRefType |
| @ | SIF_RefObject | M |  | Values: BusRouteDetail |
|  | DestinationPoint | O | GUID that identifies the bus stop/route where the student gets off the bus. | IdRefType |
| @ | SIF_RefObject | M |  | values: BusRouteDetail |
|  | DestinationPoint /ArrivalTime | O | The time that the bus associated with this route will stop at this bus stop. | xs:time |
|  | DestinationPoint /RouteNumber | O | A unique identifier for the route. F or instance, you may have route 16AM in the morning and a 16PM in the afternoon. | xs:normalizedString |
|  | DestinationPoint /RouteDescription | O | Short explanation of the route. It may be used to designate an area, or used to color-code bus routes (the "orange" route). | xs:string |
|  | DestinationPoint /VehicleNumber | O | Vehicle number of the bus. | xs:normalizedString |
|  | DestinationPoint/BusStopDescription | O | An explanation of this location. | xs:string |
|  | SIF_Metadata | O |  | SIF_Metadata |
|  | SIF_ExtendedElements | O |  | SIF_ExtendedElements |

## Issues

- Should we consider a “Distance” common element?

## XML Example

<StudentTransportInfo RefId="D3E34B359D75101A8C3D00AA001A1652"

StudentPersonalRefId="C2F23F450B86234B9B3D00AA001A1652"

Type="Inbound"

DayOfWeek="MoWeFr"

SchoolInfoRefId="B7A34E561C97345C0A4E11BB112B2753">

<TransportationStatus>2060</TransportationStatus>

<StateAidQualification>2065</StateAidQualification>

<PublicExpense>2068</PublicExpense>

<StopToSchoolDistance Unit=”m”>2.0</StopToSchoolDistance>

<WalkToStopDistance Unit=”m”>.4</WalkToStopDistance>

<HomeToSchoolDistance Unit=”m”>2.4</HomeToSchoolDistance>

<OriginPoint BusRouteDetailRefId="AAE34B359D75101A8C3D00AA001A1652">

<ArrivalTime>09:10:00</ArrivalTime>

<RouteNumber>134A</RouteNumber>

<RouteDescription>RiverFront</RouteDescription>

<VehicleNumber>16</VehicleNumber>

<BusStopDescription>Elm St @ Pine Ave</BusStopDescription>

</OriginPoint>

<DestinationPoint BusRouteDetailRefId="AAE34B359D75101A8C3D00AA001A1652">

<ArrivalTime>09:31:00</ArrivalTime>

<RouteNumber>134P</RouteNumber>

<RouteDescription>RiverFront</RouteDescription>

<VehicleNumber>16</VehicleNumber>

<BusStopDescription>George Washington Elementary West</BusStopDescription>

</DestinationPoint>

</StudentTransportInfo>

# Use Cases

## StudentTransportInfo - Request

| USE CASE : | Title: Request Use Case SIFObject: : StudentTransportInfo Use Case Number: 1 History: Initial draft; 7/25/2007 Date: 7/25/2007 |
| --- | --- |
| Use Case Type (Mandatory or Optional) | Mandatory |
| SIF Versions and References | SIF Implementation Specification 2.2 |
| Summary | The Student Information System (SIS) needs to synchronize with the Transportation system in order to present accurate transportation details for it’s students. The SIS agent sends a request for all StudentTransportInfo objects to the ZIS. The ZIS forwards the request to the default provider. The default provider (Transportation agent) responds with the StudentTransportInfo objects. |
| Actors | Student Information System/Requesting Agent Zone Integration Server Transportation System/Responding Agent |
| Preconditions | SIS Agent is registered and authorized to request StudentTransportInfo Object. Transportation agent is registered as provider of StudentTransportInfo Object |
| Post Conditions | None |
| SIF Mandatory Objects | StudentTransportInfo |
| SIF Optional Objects | None |
| Open Issues | None |

## StudentTransportInfo – Change event processing

| USE CASE : | Title: Change Event Use Case SIFObject: : StudentTransportInfo Use Case Number: 2 History: Initial draft; 7/25/2007 Date: 7/25/2007 |
| --- | --- |
| Use Case Type (Mandatory or Optional) | Mandatory |
| SIF Versions and References | SIF Implementation Specification 2.2 |
| Summary | The Student Information System (SIS) application needs to present Student transportation details (Bus number, Bus Stop and Pickup time). The SIS Agent subscribes to StudentTransportInfo objects. A modification is made to a bus route that causes some stop times to change along the route. The Transportation agent sends a StudentTransportInfo change event for all students whose pickup time has changed. |
| Actors | Student Information System/Requesting Agent Zone Integration Server Transportation System/Responding Agent |
| Preconditions | SIS Agent is registered and is a subscriber of the StudentTransportInfo Object. Transportation agent is registered as provider of StudentTransportInfo Object |
| Post Conditions | None |
| SIF Mandatory Objects | StudentTransportInfo |
| SIF Optional Objects | None |
| Open Issues | None |